## Slide 1: Satcom Chipset Evaluation
Incubating Center
2025.09.11
Confidential

## Slide 2: Test Setup & Test Result
Chipset Evaluation Board
Test Evaluation Board Trace Loss
VNA (Vector Network Analyzer) Setup
SG-PM (Signal Generator-Power Meter) Setup
VNA-NF (Signal Analyzer-Noise Figure) Setup
Test Result Summary

## Slide 3: Documents for Test Procedure
[ CLI User's Guide ]
[ IC Datasheet ]
[ SPI Interface User Guide ]
  Basic materials for chipset review
[ PA / LNA Bias LUTs ]
[ Reference Source Code ]
[ Register Map/Beam book Memory Map ]
  Stampede 2731 TX
  Blueway 1721 RX
  Stampede 2731LP TX

## Slide 4: Satcom Chipset Evaluation Board
  (Front)
  (Back)
  TX/RX IC evaluation board designed for UK customer, with specifications similar to Broad Market IC.
  (TX 2731)
  (RX 1721)
UK Company
UK Company
  Evaluation Board

## Slide 5: Test Evaluation Board Trace Loss
Chart: Frequency (GHz)
| 17.7 | 18.5 | 19.5 | 20 | 20.7 | 21.2 | 27.5 | 28.7 | 29.5 | 30 | 31
IO_H | 2.1349 | 2.2273 | 2.307 | 2.3762 | 2.4293 | 2.5188 | 3.0125 | 3.14 | 3.1591 | 3.3124 | 3.2637
IO_V | 2.1349 | 2.2273 | 2.307 | 2.3762 | 2.4293 | 2.5188 | 3.0125 | 3.14 | 3.1591 | 3.3124 | 3.2637
H0 | 1.7147 | 1.7856 | 1.8526 | 1.9066 | 1.9496 | 2.0211 | 2.4182 | 2.5211 | 2.5351 | 2.6589 | 2.6183
H1 | 1.3127 | 1.383 | 1.4336 | 1.4543 | 1.4703 | 1.5278 | 1.9044 | 1.899 | 1.9764 | 2.0233 | 2.1388
H2 | 1.7147 | 1.7856 | 1.8526 | 1.9066 | 1.9496 | 2.0211 | 2.4182 | 2.5211 | 2.5351 | 2.6589 | 2.6183
H3 | 1.3127 | 1.383 | 1.4336 | 1.4543 | 1.4703 | 1.5278 | 1.9044 | 1.899 | 1.9764 | 2.0233 | 2.1388
V0 | 1.3127 | 1.383 | 1.4336 | 1.4543 | 1.4703 | 1.5278 | 1.9044 | 1.899 | 1.9764 | 2.0233 | 2.1388
V1 | 1.7147 | 1.7856 | 1.8526 | 1.9066 | 1.9496 | 2.0211 | 2.4182 | 2.5211 | 2.5351 | 2.6589 | 2.6183
V2 | 1.3127 | 1.383 | 1.4336 | 1.4543 | 1.4703 | 1.5278 | 1.9044 | 1.899 | 1.9764 | 2.0233 | 2.1388
V3 | 1.7147 | 1.7856 | 1.8526 | 1.9066 | 1.9496 | 2.0211 | 2.4182 | 2.5211 | 2.5351 | 2.6589 | 2.6183
ka-Band | Frequency (GHz) | RF Common |  | H Pol Channels |  |  |  | V Pol Channels |  |  | 
 |  | IO_H | IO_V | H0 | H1 | H2 | H3 | V0 | V1 | V2 | V3
Downlink band | 17.7 | 2.1 | 2.1 | 1.7 | 1.3 | 1.7 | 1.3 | 1.3 | 1.7 | 1.7 | 1.3
 | 18.5 | 2.2 | 2.2 | 1.8 | 1.4 | 1.8 | 1.4 | 1.4 | 1.8 | 1.8 | 1.4
 | 19.5 | 2.3 | 2.3 | 1.9 | 1.4 | 1.9 | 1.4 | 1.4 | 1.9 | 1.9 | 1.4
 | 20.0 | 2.4 | 2.4 | 1.9 | 1.5 | 1.9 | 1.5 | 1.5 | 1.9 | 1.9 | 1.5
 | 20.7 | 2.4 | 2.4 | 1.9 | 1.5 | 1.9 | 1.5 | 1.5 | 1.9 | 1.9 | 1.5
 | 21.2 | 2.5 | 2.5 | 2.0 | 1.5 | 2.0 | 1.5 | 1.5 | 2.0 | 2.0 | 1.5
Uplink band | 27.5 | 3.0 | 3.0 | 2.4 | 1.9 | 2.4 | 1.9 | 1.9 | 2.4 | 2.4 | 1.9
 | 28.7 | 3.1 | 3.1 | 2.5 | 1.9 | 2.5 | 1.9 | 1.9 | 2.5 | 2.5 | 1.9
 | 29.5 | 3.2 | 3.2 | 2.5 | 2.0 | 2.5 | 2.0 | 2.0 | 2.5 | 2.5 | 2.0
 | 30.0 | 3.3 | 3.3 | 2.7 | 2.0 | 2.7 | 2.0 | 2.0 | 2.7 | 2.7 | 2.0
 | 31.0 | 3.3 | 3.3 | 2.6 | 2.1 | 2.6 | 2.1 | 2.1 | 2.6 | 2.6 | 2.1
Evaluation Board Trace Loss
  Check the RF cable and evaluation board trace loss in the frequency bands used for Ka-Band chipset verification.
Ka-Downlink Band
Ka-Uplink Band

## Slide 6: How to measure the trace loss
  (CH Trace dummy)
  (Common Trace dummy)
Common Path
Channel Path
➊
❷
➌
➊
❷
➌

## Slide 7: VNA Setup
  Offset Calculation
    SG (Signal Generator) : Cable Loss (w/Zero Cal.) + Channel Trace Loss
    Signal Analyzer : Cable Loss (w/Zero Cal.) + Common Trace Loss
CH_V1
CH_H1
CH_H0
CH_V0
CH_V3
CH_H3
CH_H2
CH_V2
RF_IO_V
RF_IO_H
(1) Keysight N5224B
(2) Keysight E36312A
Evaluation
(S-Parameter Test Block Diagram)
Common Loss
Channel Loss
In/Out
(1) Vector Network Analyzer
RF Cable
RF Cable
  Measurement of S-Parameters to evaluate Return Loss and Gain across the entire frequency band.
1) VNA (Vector Network Analyzer)
PA 4.0 V
I/O 1.8 V
ANA 1.8 V
DRV 1.8 V
DIG 1.0 V
(3) Power Supply
(5-Ch)
Termination

## Slide 8: SG-Power Meter Setup
  Measurement of CW and Modulation to evaluate Power, Gain and Pdc across the entire frequency band.
1) SG-SA (Signal Generator – Analyzer)
CH_V1
CH_H1
CH_H0
CH_V0
CH_V3
CH_H3
CH_H2
CH_V2
(1)
Power Meter
(2) Signal Generator
Signal Generator
Power Meter
RF_IO_V
RF_IO_H
In
Out
Out
In
RF Cable
RF Cable
Receiver Path
Transmit Path
Evaluation
Keysight N1914A
(w/ N8488 Power Sensor)
(2) Rohde SMF100A
PA 4.0 V
I/O 1.8 V
ANA 1.8 V
DRV 1.8 V
DIG 1.0 V
(3) Power Supply
(5-Ch)
(3) Keysight E36312A
Sensor
Direct
Connect
Sensor
Direct
Connect
*w/ 10 dB Attn
*w/ 10 dB Attn
  Offset Calculation
    SG (Signal Generator) : Cable Loss (w/Zero Cal.) + Channel Trace Loss
    Signal Analyzer : Cable Loss (w/Zero Cal.) + Common Trace Loss
Termination
(Tx and Rx Test Block Diagram)
Power Meter
Signal Generator
RF Cable
  Zero-Calibration
Sensor
Common Loss
Channel Loss

## Slide 9: VNA-NF Setup
  Measurement procedure
    S-Parameter Calibration(ZV-Z55), Power Calibration(NRP50S), Receiver Noise Calibration(50Ω termination)
    Hook up DUT (P1→in, out→P2), Read NF and Gain; NF21, b2/a1, NF2R, ND2 …
CH_V1
CH_H1
CH_H0
CH_V0
CH_V3
CH_H3
CH_H2
CH_V2
RF_IO_V
RF_IO_H
(1) Rodhe ZNA
(2) Rodhe ZV-Z55
Evaluation
In/Out
(1) Vector Network Analyzer
RF Cable
RF Cable
  Measurement of NF to evaluate noise figure across the entire frequency band.
PA 4.0 V
I/O 1.8 V
ANA 1.8 V
DRV 1.8 V
DIG 1.0 V
(3) Power Supply
(5-Ch)
(3) Rodhe NRP50S
1) VNA-NF (Signal Analyzer – Noise Figure)
Termination
(NF Test Block Diagram)
Common Loss
Channel Loss

## Slide 10: Test Result Summary(Datasheet, @21 dBm)
Category |  | Test Items | Results | Datasheet (Spec) | Comments (with Action Plan)
DC/ RF | Common | - Attenuation Accuracy (Common-Channel Range/Step) | Meet | Common : 16 dB / 0.50 dB Channel : 32 dB / 0.50 dB | Gain Range - Tx : 16.26 / 8.23, Rx : 16.86/ 8.01 dB (0.25 dB Attn less accurate, 0.25 not supported on Stampede and Blueway, Channel Attn measures up to 8 dB)
 |  | - Frequency vs Gain - Channel Gain Alignment | Meet | - | 8 channels /1 beam : 3.6 ~ 5 dB (Min ~ Max) (Spot calibration, etc., is required to minimize gain alignment)
 | TX | - Pin Sweep vs Pout Linearity (at OP1dB per channel) | Meet | 21 dBm | 20.14 dBm
 |  | - Pdc (Single, 8 Channels / 2 Beam) | Meet | 625 mW / 5 W | 660 mW / 4.7 W (with leakage : 19.3 mW)
 |  | Isolation | Meet | > 25 dB | 25.12 / 31.57 / 37.40 dB (Min-Typ-Max with All Band)
 |  | - EVM Bathtub Curve | (TBD) | (TBD) | *Future measurement
 | RX | - Pin Sweep vs Pout Linearity (iP1dB per channel) | Meet | -33 dBm | -38.02 dBm (Firehawk is more than the gain of Blueway. That is why iP1dB is ~ 4 dB lower)
 |  | - Pdc (Single, 8 Channels / 2 Beam) | Meet | 59.38 mW / 475 mW | 90 mW / 584 mW (with Idle Pdc : 19.3 mW) (the Blueway IC has lower gain and Pdc than the Firehawk IC reason why is one amplification stage less)
 |  | - RX Sensitivity (Pin sweep vs SNR) | (TBD) | - | *Future measurement
 |  | - Frequency vs Noise Figure (RX NF Max at Single-Channel) | Meet | 2 dB | 1.84 ~ 2.54 dB (17.7~21.2 GHz) (Need to optimized to satisfied within spec)

## Slide 11: Common Performance Evaluation
Attenuation Accuracy
Frequency vs Gain
Channel Gain Alignment
Gain vs PA / LNA Bias over temperature
Temperature Sensor Accuracy

## Slide 12: Attenuation Control
  Note
    Currently, the use of a 0.25 dB attenuation is not recommended from Sivers (i.e., the 0.25 dB Step is limited)
Common (16 dB with 0.25 dB Step)
Channel (32 dB with 0.25 dB Step)
0.25
0.5
1
2
4
8
0
1
2
3
4
5
(6-Bit)
0.25
0.5
1
2
4
8
16
0
1
2
3
4
5
6
(7-Bit)
(15.75)
(31.75)
dB / Bits | 0 | 1 | 2 | 3 | 4 | 5
0 dB | 1 | 1 | 1 | 1 | 1 | 1
0.25 dB | 0 | 1 | 1 | 1 | 1 | 1
0.50 dB | 1 | 0 | 1 | 1 | 1 | 1
0.75 dB | 0 | 0 | 1 | 1 | 1 | 1
1.00 dB | 1 | 1 | 0 | 1 | 1 | 1
2.00 dB | 1 | 1 | 1 | 0 | 1 | 1
4.00 dB | 1 | 1 | 1 | 1 | 0 | 1
8.00 dB | 1 | 1 | 1 | 1 | 1 | 0
- | - | - | - | - | - | -
15.50 dB | 1 | 0 | 0 | 0 | 0 | 0
15.75 dB | 0 | 0 | 0 | 0 | 0 | 0
(0 is enable)
dB / Bits | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 dB | 1 | 1 | 1 | 1 | 1 | 1 | 1
0.25 dB | 0 | 1 | 1 | 1 | 1 | 1 | 1
0.50 dB | 1 | 0 | 1 | 1 | 1 | 1 | 1
0.75 dB | 0 | 0 | 1 | 1 | 1 | 1 | 1
1.00 dB | 1 | 1 | 0 | 1 | 1 | 1 | 1
2.00 dB | 1 | 1 | 1 | 0 | 1 | 1 | 1
4.00 dB | 1 | 1 | 1 | 1 | 0 | 1 | 1
8.00 dB | 1 | 1 | 1 | 1 | 1 | 0 | 1
16.00 dB | 1 | 1 | 1 | 1 | 1 | 1 | 0
- | - | - | - | - | - | - | -
31.75 dB | 0 | 0 | 0 | 0 | 0 | 0 | 0
  Designed to control gain of Common and Channel Paths by Stage-Attenuation
Control Bits
Bits
Stage Atten.(dB)

## Slide 13: TX Attenuation Accuracy
Chart: Channel Attn
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Gain (dB) | 28.04 | 27.9048 | 27.7583 | 27.6561 | 27.1974 | 27.0588 | 26.9422 | 26.8134 | 26.1402 | 26.0007 | 25.8461 | 25.7339 | 25.1577 | 25.0367 | 24.8797 | 24.7423 | 24.1678 | 24.0365 | 23.8852 | 23.7195 | 23.1404 | 22.9768 | 22.8313 | 22.6673 | 22.097 | 21.9174 | 21.7747 | 21.6169 | 20.9538 | 20.8311 | 20.6688 | 20.5367 | 19.6137
Ideal Gain (dB) | 28 | 27.75 | 27.5 | 27.25 | 27 | 26.75 | 26.5 | 26.25 | 26 | 25.75 | 25.5 | 25.25 | 25 | 24.75 | 24.5 | 24.25 | 24 | 23.75 | 23.5 | 23.25 | 23 | 22.75 | 22.5 | 22.25 | 22 | 21.75 | 21.5 | 21.25 | 21 | 20.75 | 20.5 | 20.25 | 20
Chart: Common Attn
  Check the Range and Step of Gain attenuation with the given Index control of Common and Channel as SG-PM test environment.
  Note
    TX-29 GHz-B0-H0 / Channel Gain is tested up to ~127 Index, but up to ~33 Index
Max - Min
(16.26 dB)
Max - Min
(8.43 dB)
18.22 dB
(Idx. 63)
28.04 dB
(Idx. 0)
19.61 dB
(Idx. 32)
**Not Uniform Gain Reduction
(Reduced like stair shape)

## Slide 14: TX Attenuation Accuracy (1 dB Step)
Chart: Channel Attn
| 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Gain (dB) | 28.04 | 27.1974 | 26.1402 | 25.1577 | 24.1678 | 23.1404 | 22.097 | 20.9538 | 19.6137
Ideal Gain (dB) | 28 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Chart: Common Attn
| 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
Gain (dB) | 34.4759 | 33.9131 | 32.6732 | 31.9367 | 30.4805 | 29.7035 | 28.3408 | 27.5449 | 25.9134 | 25.1472 | 23.8227 | 22.9841 | 21.5974 | 20.8228 | 19.5298 | 18.7128
Ideal Gain (dB) | 34.5 | 33.5 | 32.5 | 31.5 | 30.5 | 29.5 | 28.5 | 27.5 | 26.5 | 25.5 | 24.5 | 23.5 | 22.5 | 21.5 | 20.5 | 19.5
  Check the Range and Step of Gain attenuation with the given Index control of Common and Channel as SG-PM test environment.
  Note
    TX-29 GHz-B0-H0 / Channel Gain is tested up to ~127 Index, but up to ~33 Index / Except 0.25, 0.5 dB Attn. bit
Max - Min
(16.26 dB)
34.48 dB
(Idx. 0)
18.22 dB
(Idx. 63)
Max - Min
(8.43 dB)
28.04 dB
(Idx. 0)
19.61 dB
(Idx. 32)

## Slide 15: RX Attenuation Accuracy
Chart: Common Attn
Chart: Channel Attn
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Gain (dB) | 35.0552 | 34.8165 | 34.5968 | 34.3427 | 34.1584 | 33.922 | 33.6937 | 33.4595 | 33.1057 | 32.8194 | 32.585 | 32.3316 | 32.2055 | 31.9353 | 31.6969 | 31.4324 | 31.2786 | 30.9953 | 30.7567 | 30.4751 | 30.3607 | 30.0677 | 29.8273 | 29.5322 | 29.1771 | 28.8976 | 28.6868 | 28.3463 | 28.258 | 28.0063 | 27.7393 | 27.4854 | 27.0509
Ideal Gain (dB) | 35.0552 | 34.8052 | 34.5552 | 34.3052 | 34.0552 | 33.8052 | 33.5552 | 33.3052 | 33.0552 | 32.8052 | 32.5552 | 32.3052 | 32.0552 | 31.8052 | 31.5552 | 31.3052 | 31.0552 | 30.8052 | 30.5552 | 30.3052 | 30.0552 | 29.8052 | 29.5552 | 29.3052 | 29.0552 | 28.8052 | 28.5552 | 28.3052 | 28.0552 | 27.8052 | 27.5552 | 27.3052 | 27.0552
  Check the Range and Step of Gain attenuation with the given Index control of Common and Channel as SG-PM test environment.
  Note
    RX-29 GHz-B0-H0 / Channel Gain is tested up to ~127 Index, but up to ~33 Index
Max - Min
(16.86 dB)
41.48 dB
(Idx. 0)
24.62 dB
(Idx. 63)
Max - Min
(8.01 dB)
35.06 dB
(Idx. 0)
27.05 dB
(Idx. 32)
**Not Uniform Gain Reduction
(Reduced like stair shape)

## Slide 16: RX Attenuation Accuracy (1 dB Step)
Chart: Common Attn
| 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
Gain (dB) | 41.4762 | 40.8725 | 39.3807 | 38.5762 | 37.1403 | 36.2015 | 35.0392 | 34.0474 | 32.8577 | 31.8068 | 30.7078 | 29.5821 | 28.4188 | 27.2197 | 26.1364 | 24.8401
Ideal Gain (dB) | 41.4762 | 40.4762 | 39.4762 | 38.4762 | 37.4762 | 36.4762 | 35.4762 | 34.4762 | 33.4762 | 32.4762 | 31.4762 | 30.4762 | 29.4762 | 28.4762 | 27.4762 | 26.4762
Chart: Channel Attn
| 0 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
Gain (dB) | 35.0552 | 34.1584 | 33.1057 | 32.2055 | 31.2786 | 30.3607 | 29.1771 | 28.258 | 27.0509
Ideal Gain (dB) | 35.0552 | 34.0552 | 33.0552 | 32.0552 | 31.0552 | 30.0552 | 29.0552 | 28.0552 | 27.0552
Max - Min
(16.86 dB)
  Check the Range and Step of Gain attenuation with the given Index control of Common and Channel as SG-PM test environment.
  Note
    RX-29 GHz-B0-H0 / Channel Gain is tested up to ~127 Index, but up to ~33 Index / Except 0.25, 0.5 dB Attn. bit
Max - Min
(8.01 dB)
35.06 dB
(Idx. 0)
27.05 dB
(Idx. 32)
41.48 dB
(Idx. 0)
24.62 dB
(Idx. 63)

## Slide 17: Channel Gain Alignment (TX)
  Using a VNA, verify the gain alignment accuracy for each channel of 8 channels/1 beam
  Note
    Fc: 28 GHz, Typical Gain (Common atten index : 28, Channel atten index : 0), All channel enable (H0:3, V0:3),
≑ 5 dB
Need to calibration for each channel
Chart: Gain Alignment for each channel

## Slide 18: TX Performance Evaluation
Pin Sweep vs Pout Linearity (OP1dB)
  Single channel
  8 Channels / 2 Beam
Isolation (> 25 dB)
EVM Bathtub Curve (Pin Sweep vs EVM)

## Slide 19: TX Pin Sweep vs Pout Linearity (Single Channel)
Chart: Pout Linearity
| -27.788557938329291 | -25.788557938329291 | -24.788557938329291 | -23.788557938329291 | -22.788557938329291 | -21.788557938329291 | -20.788557938329291 | -19.788557938329291 | -18.798167878329291 | -17.79234837832929 | -16.791466578329299 | -15.77857627832929 | -14.78223057832929 | -13.779687978329299 | -12.789608738329299 | -11.7769856183293 | -10.77988928832929 | -9.7432928083292936 | -8.7413154483292939 | -7.7369648983292931 | -6.7297950783292944 | -5.7371134683292944 | -4.737231468329294 | -3.7316717933292942 | -2.7530267196292941 | -1.725446398329294 | -0.73123529832929401 | 0.261882251670706 | 1.246975401670706 | 2.2497932916707071 | 3.263904561670707 | 4.2588655216707068
Pout (dBm) | -0.96688 | 1.0621 | 2.1097 | 3.1072 | 4.125 | 5.1276 | 6.1802 | 7.1728 | 8.2227 | 9.2522 | 10.2995 | 11.3523 | 12.3816 | 13.3737 | 14.4738 | 15.5092 | 16.5464 | 17.4727 | 18.3606 | 19.1266 | 19.7294 | 20.1431 | 20.4295 | 20.633 | 20.7661 | 20.856 | 20.9089 | 20.9432 | 20.9698 | 20.988 | 20.9963 | 21.0031
Gain (dB) | 26.8217 | 26.8506 | 26.8983 | 26.8958 | 26.9135 | 26.9162 | 26.9688 | 26.9614 | 27.0208 | 27.0445 | 27.091 | 27.1309 | 27.1638 | 27.1533 | 27.2634 | 27.2862 | 27.3263 | 27.216 | 27.102 | 26.8635 | 26.4592 | 25.8802 | 25.1668 | 24.3646 | 23.5192 | 22.5814 | 21.6401 | 20.6813 | 19.7228 | 18.7382 | 17.7324 | 16.7442
Psum (W) | 0.28618 | 0.28913 | 0.29011 | 0.29182 | 0.29415 | 0.29619 | 0.29953 | 0.30388 | 0.30927 | 0.31593 | 0.32374 | 0.33416 | 0.34657 | 0.3646 | 0.38691 | 0.41393 | 0.44828 | 0.48622 | 0.53126 | 0.57886 | 0.62236 | 0.65843 | 0.68793 | 0.71309 | 0.7318 | 0.74653 | 0.75755 | 0.76506 | 0.77091 | 0.77545 | 0.77866 | 0.78005
  Using a SG-SA, verify the power saturation, OP1dB, Pdc.
  Note
    TX-29 GHz-B0-H0
OP1dB

## Slide 20: TX Pin Sweep vs Pout Linearity (8 Channels / 2 Beam)
  Using a SG-SA, verify the power saturation, OP1dB, Pdc.
  Note
    TX-29 GHz-B0-H0
Chart: Pout Linearity
| -27.788557938329291 | -25.788557938329291 | -24.788557938329291 | -23.788557938329291 | -22.788557938329291 | -21.788557938329291 | -20.788557938329291 | -19.788557938329291 | -18.798167878329291 | -17.79234837832929 | -16.791466578329299 | -15.77857627832929 | -14.78223057832929 | -13.779687978329299 | -12.789608738329299 | -11.7769856183293 | -10.77988928832929 | -9.7432928083292936 | -8.7413154483292939 | -7.7369648983292931 | -6.7297950783292944 | -5.7371134683292944 | -4.737231468329294 | -3.7316717933292942 | -2.7530267196292941 | -1.725446398329294 | -0.73123529832929401 | 0.261882251670706 | 1.246975401670706 | 2.2497932916707071 | 3.263904561670707 | 4.2588655216707068
Pout (dBm) | -7.391 | -5.4084 | -4.4175 | -3.4278 | -2.458 | -1.4663 | -0.47629 | 0.50437 | 1.5021 | 2.488 | 3.4865 | 4.5055 | 5.4762 | 6.4586 | 7.4034 | 8.0625 | 9.1792 | 10.2508 | 11.357 | 12.4612 | 13.561 | 14.6771 | 15.7088 | 16.7166 | 17.612 | 18.4047 | 19.0412 | 19.5103 | 19.7815 | 19.9427 | 20.0552 | 20.1223
Gain (dB) | 20.3975 | 20.3802 | 20.371 | 20.3608 | 20.3306 | 20.3222 | 20.3123 | 20.2929 | 20.3003 | 20.2804 | 20.278 | 20.2841 | 20.2584 | 20.2383 | 20.193 | 19.8395 | 19.9591 | 19.9941 | 20.0983 | 20.1981 | 20.2908 | 20.4142 | 20.446 | 20.4483 | 20.3651 | 20.1302 | 19.7724 | 19.2484 | 18.5346 | 17.6929 | 16.7913 | 15.8634
Psum (W) | 2.4264 | 2.4184 | 2.4192 | 2.4212 | 2.4197 | 2.4198 | 2.4222 | 2.4225 | 2.424 | 2.4297 | 2.4334 | 2.4375 | 2.4413 | 2.4456 | 2.4464 | 2.4021 | 2.4595 | 2.5301 | 2.6245 | 2.7504 | 2.9122 | 3.1149 | 3.3754 | 3.6803 | 4.0199 | 4.3702 | 4.7004 | 4.9759 | 5.1706 | 5.2842 | 5.3776 | 5.4447
OP1dB

## Slide 21: Isolation (> 25 dB)
  Using a VNA, verify the isolation of channel between H and V, as well as the dual stream between channels
  Note
    Typical Gain (Common atten index : 28, Channel atten index : 0)
Isolation Requirement | Spec | B0-H0 to B0-V0 (Min) | B0-H0 to B0-V0 (Avg) | B0-H0 to B0-V0 (Max)
Osprey 2731 | > 25 dB | -25.12 dB | -31.57 | -37.40
Chart: Channel Isolation

## Slide 22: RX Performance Evaluation
Pin Sweep vs Pout Linearity (iP1dB)
  Single channel
  8 Channels / 2 Beam
RX Sensitivity (Pin sweep vs SNR)
Frequency vs Noise Figure

## Slide 23: RX Pin Sweep vs Pout Linearity (Single Channel)
  Note
    RX-29 GHz-B0-H0
Chart: Pout Linearity
| -54.020450186761437 | -52.020450186761437 | -50.020450186761437 | -48.020450186761437 | -46.020450186761437 | -44.020450186761437 | -42.020450186761437 | -40.020450186761437 | -38.020450186761437 | -36.020450186761437 | -34.020450186761437 | -33.020450186761437 | -32.020450186761437 | -31.02045018676144 | -30.02045018676144 | -29.02045018676144 | -28.02045018676144 | -27.02045018676144 | -26.02045018676144 | -25.02045018676144 | -24.02045018676144 | -23.02045018676144 | -22.02045018676144 | -21.02045018676144 | -20.02045018676144 | -19.02045018676144 | -18.02045018676144 | -17.021828766761441 | -16.018493766761431 | -15.020379966761441 | -14.021508466761439 | -13.020039966761439 | -12.01370876676144
Pin (dBm) | -54.0205 | -52.0205 | -50.0205 | -48.0205 | -46.0205 | -44.0205 | -42.0205 | -40.0205 | -38.0205 | -36.0205 | -34.0205 | -33.0205 | -32.0205 | -31.0205 | -30.0205 | -29.0205 | -28.0205 | -27.0205 | -26.0205 | -25.0205 | -24.0205 | -23.0205 | -22.0205 | -21.0205 | -20.0205 | -19.0205 | -18.0205 | -17.0218 | -16.0185 | -15.0204 | -14.0215 | -13.02 | -12.0137
Gain (dB) | 34.7372 | 34.9443 | 34.9762 | 35.0346 | 35.0266 | 34.9543 | 34.8026 | 34.5165 | 33.9833 | 33.0866 | 31.6691 | 30.7648 | 29.7474 | 28.6335 | 27.4622 | 26.2447 | 25.005 | 23.7638 | 22.541 | 21.3329 | 20.153 | 19.0178 | 17.9 | 16.812 | 15.7361 | 14.6754 | 13.628 | 12.5965 | 11.5575 | 10.5434 | 9.5451 | 8.5444 | 8.5444
Psum (W) | 0.08857 | 0.08883 | 0.088935 | 0.088919 | 0.088993 | 0.089182 | 0.089355 | 0.089609 | 0.089903 | 0.090465 | 0.090919 | 0.091124 | 0.091415 | 0.091684 | 0.091936 | 0.09225 | 0.09269 | 0.093069 | 0.093593 | 0.094172 | 0.094909 | 0.095418 | 0.09623 | 0.096956 | 0.0977 | 0.09849 | 0.099853 | 0.10138 | 0.10237 | 0.10366 | 0.10488 | 0.1053 | 0.1053
iP1dB
  Using a SG-SA, verify the iP1dB, and Pdc

## Slide 24: RX Pin Sweep vs Pout Linearity (8 Channels/2 Beam)
  Note
    RX-29 GHz-B0-H0
Chart: Pout Linearity
| -54.020450186761437 | -52.020450186761437 | -50.020450186761437 | -48.020450186761437 | -46.020450186761437 | -44.020450186761437 | -42.020450186761437 | -40.020450186761437 | -38.020450186761437 | -36.020450186761437 | -34.020450186761437 | -33.020450186761437 | -32.020450186761437 | -31.02045018676144 | -30.02045018676144 | -29.02045018676144 | -28.02045018676144 | -27.02045018676144 | -26.02045018676144 | -25.02045018676144 | -24.02045018676144 | -23.02045018676144 | -22.02045018676144 | -21.02045018676144 | -20.02045018676144 | -19.02045018676144 | -18.02045018676144 | -17.021828766761441 | -16.018493766761431 | -15.020379966761441 | -14.021508466761439 | -13.020039966761439 | -12.01370876676144
Pin (dBm) | -54.0205 | -52.0205 | -50.0205 | -48.0205 | -46.0205 | -44.0205 | -42.0205 | -40.0205 | -38.0205 | -36.0205 | -34.0205 | -33.0205 | -32.0205 | -31.0205 | -30.0205 | -29.0205 | -28.0205 | -27.0205 | -26.0205 | -25.0205 | -24.0205 | -23.0205 | -22.0205 | -21.0205 | -20.0205 | -19.0205 | -18.0205 | -17.0218 | -16.0185 | -15.0204 | -14.0215 | -13.02 | -12.0137
Gain (dB) | 29.1475 | 29.6014 | 29.8177 | 30.0071 | 30.0656 | 30.1133 | 30.0637 | 29.9432 | 29.726 | 29.3493 | 28.7026 | 28.2391 | 27.674 | 27.0114 | 26.2344 | 25.3422 | 24.3616 | 23.3065 | 22.1946 | 21.0569 | 19.9198 | 18.7962 | 17.6987 | 16.6294 | 15.601 | 14.6163 | 13.6849 | 12.8055 | 11.9518 | 11.1232 | 10.3218 | 9.5398 | 8.7701
Psum (W) | 0.57564 | 0.58006 | 0.5807 | 0.5804 | 0.58087 | 0.58136 | 0.58136 | 0.58154 | 0.58196 | 0.58284 | 0.58367 | 0.58414 | 0.58474 | 0.58537 | 0.58626 | 0.58692 | 0.58765 | 0.5891 | 0.59002 | 0.59138 | 0.59238 | 0.59377 | 0.59495 | 0.59667 | 0.5982 | 0.59985 | 0.60164 | 0.60374 | 0.60582 | 0.60786 | 0.60903 | 0.61088 | 0.61225
iP1dB
  Using a SG-SA, verify the iP1dB, and Pdc

## Slide 25: RX Frequency vs Noise Figure
  Note
    RX-B0-H0, RX-B1-V0
Chart: Noise Figure
| 17.7 | 17.8 | 17.899999999999999 | 18 | 18.100000000000001 | 18.2 | 18.3 | 18.399999999999999 | 18.5 | 18.600000000000001 | 18.7 | 18.8 | 18.899999999999999 | 19 | 19.100000000000001 | 19.2 | 19.3 | 19.399999999999999 | 19.5 | 19.600000000000001 | 19.7 | 19.8 | 19.899999999999999 | 20 | 20.100000000000001 | 20.2 | 20.3 | 20.399999999999999 | 20.5 | 20.6 | 20.7 | 20.8 | 20.9 | 21 | 21.1 | 21.2
NF (dB) | 1.963 | 2.0736 | 2.0468 | 2.056 | 2.0408 | 1.9621 | 1.8352 | 1.9321 | 2.0053 | 1.9381 | 1.9227 | 1.9782 | 1.9899 | 1.9937 | 2.1338 | 2.3132 | 2.1052 | 2.1465 | 2.2879 | 2.0478 | 1.9095 | 2.1244 | 2.0411 | 1.9248 | 2.1862 | 2.233 | 2.2184 | 2.2823 | 2.4446 | 2.466 | 2.3625 | 2.4404 | 2.4896 | 2.4956 | 2.406 | 2.5393
NF (dB) | 1.9285 | 1.9661 | 2.0084 | 1.9985 | 2.0355 | 2.0885 | 1.8983 | 1.9311 | 2.1315 | 1.9412 | 1.8834 | 2.0469 | 2.1411 | 1.9773 | 2.1378 | 2.2459 | 2.156 | 2.0394 | 2.2448 | 2.1345 | 1.9368 | 2.1051 | 2.0117 | 1.9594 | 2.0584 | 2.0198 | 2.0782 | 2.1919 | 2.26 | 2.4741 | 2.2265 | 2.3847 | 2.4178 | 2.4701 | 2.4282 | 2.5203
  Using a VNA-NF, Noise Figure Measurement in 17.7 to 21.2 GHz Band Range